## Slide 1: L08 Electronic Mail
Dr. Ram P Rustagi
rprustagi@ksit.edu.in
http://www.rprustagi.com
https://www.youtube.com/rprustagi
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 2
Ram P Rustagi/CSE/KSIT
CN-Basic-L14-HTTP-Overview
Resources Acknowledgement

## Slide 3: Electronic mail
Three major components:
user agents
mail servers
simple mail transfer protocol: SMTP (RFC 5321)
  obsoletes RFC 2821
User Agent
a.k.a. “mail reader”
composing, editing, reading mail messages
e.g.: Applications: Outlook, Thunderbird, Mail(Apple)
Outgoing, incoming messages stored on server
user mailbox
outgoing
message queue
mail
server
mail
server
mail
server
SMTP
SMTP
SMTP
user
agent
user
agent
user
agent
user
agent
user
agent
user
agent
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 4: Email: General scenario
Src (fig): Forouzan - Computer Networking
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 5: Electronic mail: mail servers
mail servers:
mailbox contains incoming messages for user
message queue of outgoing (to be sent) mail messages
SMTP protocol between mail servers to send email messages
  client: sending mail server
  “server”: receiving mail server
mail
server
mail
server
mail
server
SMTP
SMTP
SMTP
user
agent
user
agent
user
agent
user
agent
user
agent
user
agent
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 6: Email - User Agent
User Agent functions
  Compose
    send
  Read
  Reply
  Forward
  Delete
  Handling Mailboxes
Command line UAs
  Mail, mailx, pine, elm etc
GUI UAs
  iMail, Eudora, Outlook, Thunderbird etc
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 7: Electronic Mail: SMTP [RFC 2821]
uses TCP to reliably transfer email message from client to server, port 25 (unsecure)
  secure ports (465, 587)
direct transfer: sending server to receiving server
three phases of transfer
  handshaking (greeting)
  transfer of messages
  closure
command/response interaction (like HTTP, FTP)
  commands: ASCII text
  response: status code and phrase
messages must be in 7-bit ASCII
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 8: Scenario: Alice sends message to Bob
1) Alice uses UA to compose message “to” bob@someschool.edu
2) Alice’s UA sends message to her mail server; message placed in message queue
3) client side of SMTP opens TCP connection with Bob’s mail server
4) SMTP client sends Alice’s message over the TCP connection
5) Bob’s mail server places the message in Bob’s mailbox
6) Bob invokes his user agent to read message
mail
server
mail
server
user
agent
1
2
3
4
Alice’s mail server
5
Bob’s mail server
6
user
agent
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 9: Sample SMTP interaction
$ nc 10.211.55.10 25
  Trying 10.211.55.10...
  Connected to 10.211.55.10.
  Escape character is '^]'.
  220 ubuntu.localdomain ESMTP Postfix (Ubuntu)
HELO ksit.edu.in
  250 ubuntu.localdomain
MAIL FROM: rprustagi@ksit.edu.in
  250 2.1.0 Ok
RCPT TO: dummy@ksit.local
  250 2.1.5 Ok
RCPT TO: dummyuser@ksit.local
  250 2.1.5 Ok
DATA
  354 End data with <CR><LF>.<CR><LF>
Subject: mail trial with postfix
This is a test mail to try that POP and IMAP works
with mail delivery.
  250 2.0.0 Ok: queued as 89715362D67
QUIT
221 2.0.0 Bye
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 10: Try SMTP interaction for yourself:
nc servername 25
see 220 reply from server
enter HELO, MAIL FROM, RCPT TO, DATA, QUIT commands
  Current EHLO is used in place of HELO
above lets you send email without using email client (reader)
Sending multiple mails in a single connection
Start with MAIL FROM after .(period)
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 11: SMTP: and HTTP
SMTP uses persistent connections
SMTP requires message (header & body) to be in 7-bit ASCII
SMTP server uses CRLF to determine end of message
comparison with HTTP:
HTTP: pull
SMTP: push
Similarities
  ASCII command/response interaction
  status codes
Differences
  HTTP: each object encapsulated in its own response msg
  SMTP: multiple objects sent in multipart msg
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 12: SMTP : Miscellaneous details
Secure SMTP: RFC 4954
  Uses AUTH command
    E.g AUTH DIGEST-MD5
    Uses SASL (RFC 4422)
      Simple Authentication and Secure Layer
  Plaintext password is not to be used
Mail Exchange (MX) Records
  DNS provides this information
Sendmail daemon
  On unix systems
Internationalized Email: RFC 6351
  vCard
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 13: Mail message format
SMTP: protocol for exchanging email msgs
RFC 822: standard for text message format:
header lines, e.g.,
  To:
  From:
  Subject:
  different from SMTP
  MAIL FROM, RCPT TO: commands!
Body: the “message”
  ASCII characters only
header
body
blank
line
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 14: Email
RFC 822 (obsoleted by 2822) initially defined message structure
Header and body
Header separated by body with a blank line
Header is a series of lines terminated by <CR><LF>
Header format is type: value
To:, Subject:, Date:, Received: etc
More details, see RFC 822 (or 2822)
RFC 822 extended in 1993/96
To carry different (than text) types of data
Audio, video, word docs, images,
MIME (Multipurpose Internet Mail Extension) format
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 15: Mail access protocols
SMTP: delivery/storage to receiver’s server
mail access protocol: retrieval from server
  POP: Post Office Protocol [RFC 1939]: authorization, download
  IMAP: Internet Mail Access Protocol [RFC 3501]: more features, including manipulation of stored msgs on server
  HTTP: Gmail, Hotmail, Yahoo! Mail, etc.
sender’s mail
server
SMTP
SMTP
mail access
protocol
receiver’s mail
server
(e.g., POP,
IMAP)
user
agent
user
agent
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 16: POP3
RFC 1939
Basic operation
  Server listens on port 110 (Default)
  Client connects to the POP3 server
  Client issues commands (case insensitive) with args
    Typically 4 (or 3) character long keywords
  Response consists of
    status code, keyword, additional information
    Two status indicators: “+OK”, “-ERR”
  Session goes thru
    Authorization state
    Transaction state
    Update and goodbye
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 17: POP3 protocol
authorization phase
client commands:
  user: declare username
  pass: password
  Alternatively APOP command
server responses
  +OK
  -ERR
transaction phase, client:
list: list message numbers
retr: retrieve message by number
dele: delete
quit
C: list
S: 1 498
S: 2 912
S: .
C: retr 1
S: <message 1 contents>
S: .
C: dele 1
C: retr 2
S: <message 1 contents>
S: .
C: dele 2
C: quit
S: +OK POP3 server signing off
S: +OK POP3 server ready
C: user bob
S: +OK
C: pass hungry
S: +OK user successfully logged on
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 18: MIME Based Email
MIME based message structure
Collection of Header lines
Augment the original RFC822 headers
Describe the ways in which data is carried
Content type and sub-types
Defines how the content is to be interpreted
Encoding of various data types
Enables sending of data as an ASCII email msg
Intermediate gateways require
That email content be ASCII
Base64:
3 bytes of data represented in 4 bytes
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 19: MIME Based Email
Email Header
  MIME-Version: 1.1
  Content-Type: <type/subtype>
  Content-Transfer-Encoding: <encoding type>
    7-bit, 8-bit, Base64, Binary, Quoted printable
  Content-Id: <message id>
  Content-Description: textual explanation
Examples:
  Ch02-SMTP-attachment.pcap
  Look at MIME headers
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 20: Base64 encoding
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 21: Base64 encoding
Encode 18CS into base 64.
Write 18CS (ASCII) in hex/binary
  Hex: 0x31384353
  Binary: 00110001 00111000 01000011 01010011
Divide in blocks of 6 bits
  001100 010011 100001 000011 010100 110000
  (12) (19) (33) (3) (20) (48)
Index with these value in Base64 table
  M(12) T(19) h(33) D(3) U(20) w(48)
  Encoded characters should be in blocks of 4.
  Add two filler characters ‘==‘
Base64 encoded value
  MThDUw==
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 22: Installing Mail programs
On Ubuntu
  https://help.ubuntu.com/community/PostfixBasicSetupHowto
  sudo apt-get install mailutils
  sudo apt-get install courier-pop
  sudo apt-get install courier-imap
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 23: POP3 (more) and IMAP
more about POP3
previous example uses POP3 “download and delete” mode
  Bob cannot re-read e-mail if he changes client
POP3 “download-and-keep”: copies of messages on different clients
POP3 is stateless across sessions
IMAP (RFC 3501)
keeps all messages in one place: at server
allows user to organize messages in folders
keeps user state across sessions:
names of folders and mappings between message IDs and folder name
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 24: POP3 vs IMAP4
POP3 deficiencies
Does not allow user to organize mails on server
User can not have different folders on server
Use can create folders on local system
Does not allow partial email content check
IMAP4 features
User can check email header prior to download
User can search the contents prior to download
Allows partial download (MIME multipart)
User can create, delete, rename mailboxes
can create a hierarchy of mailboxes
Web based email
Using HTTP with a email website
Hotmail, gmail, etc
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email

## Slide 25: Summary
User Agent
Mail agent
Mail transfer protocol
  SMTP, POP3, IMAP4
Mail authorization
ASCII text
MIME email
  uses Base64 encoding
Ram P Rustagi/CSE/KSIT
18CS52-CN-L08-Email